## Slide 1: Human/AT Interface Cook and Hussey, Chapter 7
Damian Gordon

## Slide 2
What is Assistive Technology?
“Any product, instrument, equipment or technical system used by a disabled or elderly person, made specially or existing on the market, aimed to prevent, compensate, relieve or neutralise the deficiency, the inability or the handicap.”
International ISO-9999 Standard
Recall from a previous lecture

## Slide 3
Last Week

## Slide 4
Human
Activity
Assistive
Technology
Context
HAAT Model
Physical
Cognitive
Emotional
Novice vs. Expert
Physical
Social
Cultural
Institutional
- Self Care
Productivity
Leisure
HTI
Activity Output
Processor
Environmental Interface

## Slide 5: Individual and Group Challenge
The earliest record of wheelchairs date back to the 6th century, and were found inscribed on a stone slate in China.
Redesign the wheelchair for the 21st century, consider the new materials, methods of propulsion, etc. (15 mins.)
Now combine your ideas together in pairs. (10 mins.)
Come up to the board and draw a picture.

## Slide 6: Individual and Group Challenge
Josep Mora, designer from Barcelona, adapts this vehicle for people with reduced mobility. There is a hand break to keep the vehicle standing on its own when stopped

## Slide 7
HAAT Model
Activity
Human
Context
Activity
Output
Processor
Environmental
Interface
HTI

## Slide 8
Human/AT Interface
“the boundary shared by interacting components in a system” in which “the essence of this interaction is communication or the exchange of information back and forth across the boundary”

## Slide 9: Elements of the Interface
CONTROL INTERFACE: The hardware by which a human operates or controls a device, e.g. keyboard, joystick.
SELECTION SET: These are the items available to select from.
SELECTION METHODS: The user can select using the control interface either by Direct Selection or Indirect Selection.

## Slide 10: Elements of the Interface
Control
Interface
Selection
Methods
Selection
Set

## Slide 11: Elements of the Interface
CONTROL INTERFACE
The hardware by which a human operates or controls a device, e.g. keyboard, joystick.
Also known as the Input Device.
It can generate any number of independent inputs, from one to infinity (called the Input Domain).

## Slide 12: Elements of the Interface
CONTROL INTERFACE
A keyboard may have around 100 keys, each representing a different symbol, whereas a switch may one have one signal.
These are examples of Discrete Inputs.

## Slide 13: Elements of the Interface
CONTROL INTERFACE
When considering a volume control typically there are an infinite number of values it can have. The number of positions of a mouse ball, or the positions of a steering wheel are also infinite.
These are examples of Continuous Inputs.

## Slide 15: Elements of the Interface
CONTROL INTERFACES: CHARACTERISTICS
Spatial Characteristics are
  The overall physical size, dimensions, shape weight.
  The number of available targets contained within the interface.
  The size of each target.
  The spacing between targets.

## Slide 16: Elements of the Interface
CONTROL INTERFACES: CHARACTERISTICS
Activation and Deactivation Characteristics are
  Method of Activation: The way in which the user sends the signal.
  Effort: The amount of effort required to send the signal.
  Displacement: How far a control interface travels from its original position.
  Deactivation: Opposite to activation.
  Flexibility: The number of ways the controls can be operated.
  Durability and Maintainability: Durability and maintainability of the interface.

## Slide 17
Elements of the Interface: Method of Activation
User Action | Signal Detected | Examples
1. Movement (eye, head, tongue, arms, leg) | 1a. Mechanical control interface, activation by application of force | 1a. Joystick, keyboard
 | 1b. Electromagnetic control interface, light or radio activation | 1b. Light pointer, light detector, radio transmitter
 | 1c. Electrical control interface, detection of electrical signals from surface of body | 1c. EMG, EOG, capacitive, Contact switch,
 | 1d. Proximity control interface, movement close to device needed | 1d. Heat-sensitive switches
2. Respiration (inhalation, expiration) | 2. Pneumatic control interface, detects respiratory airflow or pressure | 2. Puff and sip
3. Phonation | 3. Sound or voice control interface, detects articulated sound or speech | 3. Sound Switch, whistle switch, speech recognition

## Slide 18: Elements of the Interface: Effort
The amount of effort required to send the signal.
Effort varies from zero to a relatively large amount.
For a mechanical interface the force needed can be significant.
For an electromagnetic interface the effort in minimised, e.g. using a light pointer.

## Slide 19: Elements of the Interface: Displacement
How far a control interface travels from its original position to its activated position.
This is unique to mechanical switches.
Force activated joysticks require some force but no displacement.
This can be useful in terms of giving feedback to the user.

## Slide 20: Elements of the Interface: Deactivation
Opposite to activation.
Typically one third or one half of the force required for activation.

## Slide 21: Elements of the Interface: Flexibility
The number of ways the controls can be operated.
Depending on the individual’s disability, they may have differences in strength, range of movement, muscle tone, sensation, or coordination.
Devices should be designed with this in mind, one person may press a button with their finger, another with their elbow, another with their thumb, another with a head pointer.

## Slide 22: Elements of the Interface: Durability and Maintainability
Durability and maintainability of the interface.
  How often will the interface be used?
  How much force will be used activating it?
  Will the user have uncontrolled movements?
  Will a more expensive metal switch be better in the long term than a cheaper plastic one?
  Can this be easily cleaned?
  Does the interface need replacements?
  Is their a loaner available while in repair?

## Slide 23: Elements of the Interface
Control
Interface
Selection
Methods
Selection
Set
Discrete Inputs
Continuous Inputs

## Slide 24: Elements of the Interface
SELECTION SET
These are the items available to select from.

## Slide 25: Elements of the Interface
SELECTION SET
These can be
  Words, letters and sentences
  Symbols including computer icons
  Line drawings
  Synthetic speech

## Slide 26: Elements of the Interface
SELECTION SET
The modalities can be
  Visual, e.g. letters on a keyboard
  Tactile, e.g. Braille
  Auditory, e.g. spoken choices in auditory scanning

## Slide 27: Elements of the Interface
SELECTION SET
The size, modality and type of selection set is chosen by the user’s needs and the desired activity output.
  e.g. an individual with good spelling skills might use a standard keyboard (with ~100 keys) whereas an individual with poor language skills or limited physical control may use one of two picture symbol choices.

## Slide 28: Elements of the Interface
Control
Interface
Selection
Methods
Selection
Set
Activity Output

## Slide 29: Elements of the Interface
SELECTION METHODS
The user can select using the control interface either by Direct Selection or Indirect Selection.
These are called the Selection Methods.

## Slide 30: Elements of the Interface
Direct Selection
The individual is able to use the control interface to randomly choose any of the items in the selection set.
Using a finger, voice, hand, eye, or some other body movement.
At any one time any selection item is equally available for selection.

## Slide 31: Elements of the Interface
Direct Selection
Typing on a keyboard, or even pick a flower from the garden are considered examples of direct selection.
Because direct selection requires refined, controlled movements, it may be difficult for individuals with special needs.

## Slide 32: Elements of the Interface
Indirect Selection
Intermediate steps are involved in making a selection
The most common approach used in scanning.

## Slide 33: Elements of the Interface
Indirect Selection
Scanning means that the selection set is presented on a display and is sequentially scanned by a cursor or a light on the display.
When the appropriate item from the selection set is highlighted, the user is required to generate a signal

## Slide 35: Elements of the Interface
Indirect Selection
Scanning
e.g. the user wishes to generate the letter “K” from the following scanning array.

## Slide 36
Elements of the Interface
Scanning
A
B
C
D
E
F
G
H
I
J
K
L
M
N
O
P
Q
R
S
T
U
V
W
X
Y
Z
@
#
T
Switch

## Slide 37
Elements of the Interface
Scanning
A
B
C
D
E
F
G
H
I
J
K
L
M
N
O
P
Q
R
S
T
U
V
W
X
Y
Z
@
#
T
Switch

## Slide 38
Elements of the Interface
Scanning
A
B
C
D
E
F
G
H
I
J
K
L
M
N
O
P
Q
R
S
T
U
V
W
X
Y
Z
@
#
T
Switch

## Slide 39
Elements of the Interface
Scanning
A
B
C
D
E
F
G
H
I
J
K
L
M
N
O
P
Q
R
S
T
U
V
W
X
Y
Z
@
#
T
Switch

## Slide 40
Elements of the Interface
Scanning
A
B
C
D
E
F
G
H
I
J
K
L
M
N
O
P
Q
R
S
T
U
V
W
X
Y
Z
@
#
T
Switch

## Slide 41
Elements of the Interface
Scanning
A
B
C
D
E
F
G
H
I
J
K
L
M
N
O
P
Q
R
S
T
U
V
W
X
Y
Z
@
#
T
Switch

## Slide 42
Elements of the Interface
Scanning
A
B
C
D
E
F
G
H
I
J
K
L
M
N
O
P
Q
R
S
T
U
V
W
X
Y
Z
@
#
T
Switch

## Slide 43
Elements of the Interface
Scanning
A
B
C
D
E
F
G
H
I
J
K
L
M
N
O
P
Q
R
S
T
U
V
W
X
Y
Z
@
#
T
Switch

## Slide 44
Elements of the Interface
Scanning
A
B
C
D
E
F
G
H
I
J
K
L
M
N
O
P
Q
R
S
T
U
V
W
X
Y
Z
@
#
T
Switch

## Slide 45
Elements of the Interface
Scanning
A
B
C
D
E
F
G
H
I
J
K
L
M
N
O
P
Q
R
S
T
U
V
W
X
Y
Z
@
#
T
Switch

## Slide 46
Elements of the Interface
Scanning
A
B
C
D
E
F
G
H
I
J
K
L
M
N
O
P
Q
R
S
T
U
V
W
X
Y
Z
@
#
T
Switch

## Slide 47
Elements of the Interface
Scanning
A
B
C
D
E
F
G
H
I
J
K
L
M
N
O
P
Q
R
S
T
U
V
W
X
Y
Z
@
#
T
Switch

## Slide 48
Elements of the Interface
Scanning
A
B
C
D
E
F
G
H
I
J
L
M
N
O
P
Q
R
S
T
U
V
W
X
Y
Z
@
#
T
K
K
Switch

## Slide 49: Group Challenge
Consider a few ways to speed up the process of getting to the letters you need (5 mins.)
Now combine your ideas with everyone else in the class. (10 mins.)

## Slide 50: Elements of the Interface
Indirect Selection
Scanning
Scanning and direct selection require different physical and cognitive skills.
Scanning requires good visual tracking skills, a high degree of attention, and the ability to sequence.
On the positive side it does require very little motor control to make a selection.

## Slide 51: Elements of the Interface
Scanning
Location of letters
Text prediction
Increase/decrease scanning rate
Change direction of scan

## Slide 52: Elements of the Interface
Indirect Selection
Directed Scanning
This is a hybrid approach in which the user can control the direction of scanning, vertical or horizontal
Requires more steps than direct scanning, but less than single-switch scanning.

## Slide 53
Elements of the Interface
Direct Scanning
A
B
C
D
E
F
G
H
I
J
K
L
M
N
O
P
Q
R
S
T
U
V
W
X
Y
Z
@
#
Joystick

## Slide 54
Elements of the Interface
Direct Scanning
A
B
C
D
E
F
G
H
I
J
K
L
M
N
O
P
Q
R
S
T
U
V
W
X
Y
Z
@
#
Joystick

## Slide 55
Elements of the Interface
Direct Scanning
A
B
C
D
E
F
G
H
I
J
K
L
M
N
O
P
Q
R
S
T
U
V
W
X
Y
Z
@
#
Joystick

## Slide 56
Elements of the Interface
Direct Scanning
A
B
C
D
E
F
G
H
I
J
K
L
M
N
O
P
Q
R
S
T
U
V
W
X
Y
Z
@
#
Joystick

## Slide 57
Elements of the Interface
Direct Scanning
A
B
C
D
E
F
G
H
I
J
K
L
M
N
O
P
Q
R
S
T
U
V
W
X
Y
Z
@
#
Joystick

## Slide 58
Elements of the Interface
Direct Scanning
A
B
C
D
E
F
G
H
I
J
K
L
M
N
O
P
Q
R
S
T
U
V
W
X
Y
Z
@
#
Joystick

## Slide 59
Elements of the Interface
Scanning
A
B
C
D
E
F
G
H
I
J
L
M
N
O
P
Q
R
S
T
U
V
W
X
Y
Z
@
#
K
K
Joystick

## Slide 60: Elements of the Interface
Indirect Selection
Another form of indirect selection is called Coded Access.
With this approach the individual uses a distinct sequence of movements to input a code for each item in the selection set.
e.g. Morse Code could be used to represent the letters (and the most common letter are the shortest codes)

## Slide 62: Morse Code

## Slide 63: Elements of the Interface
Control
Interface
Selection
Methods
Selection
Set
Direction Selection
Indirect Selection

## Slide 64: So in summary

## Slide 65: Elements of the Interface
Control
Interface
Selection
Methods
Selection
Set
Activity Output
Discrete Inputs
Continuous Inputs
Direction Selection
Indirect Selection

## Slide 66: Elements of the Interface
Devices should be designed to be accessed by more than one method
And if we can make them so they work with as many approaches as possible, we are adhering to the principal of Universal Design.

## Slide 67
Seven Principles of Universal Design
Equitable Use
Flexibility in Use
Simple and Intuitive
Perceptible Information
Tolerance for Error
Low Physical Effort
Size and Space for Approach and Use
Notes: <number>
<footer>
<header>
<date/time>
<number>

## Slide 68: Adapting the Computer
When attempting to adapt a computer, the key philosophical approach is to begin with the simplest modifications possible and then progress to more complex ones.

## Slide 69: Adapting the Computer
The term Transparent Access is used to refer to two fundamental concepts
  100% of the functions of the computer must be adapted
  All application software should be equally usable

## Slide 70: Adapting the Computer
So, in other words, all keyboard keys, including modifiers like SHIFT, CTRL, ALT, and all the mouse functions, like POINT, CLICK and DRAG must be available in the adapted system.
If you are using Microsoft Word, it should work exactly the same with or without modifications.

## Slide 71: Adapting the Computer

## Slide 72: Adapting the Computer

## Slide 73: Adapting the Computer

## Slide 74: Adapting the Computer

## Slide 75: Adapting the Computer
The term On-screen Keyboard refers to a keyboard emulation presented on-screen.
For single-switch users the on-screen keyboard can be a scanning array.

## Slide 76: Communication Aids Available
Large Button Telephone with digital answer machine
Ring Flash Amp
Memo Minder
Voice Dialer
Step Pad

## Slide 77: Vision and Reading Aids Available
Desktop Top or Screen Magnifier
Flip Automatic Page Turner
Reading Pen
Text Reading Software
Over bed Table
Lifestyle – Large Game Cards

## Slide 78: Hearing and Listening Aids Available
Telephone Amplifier
Flashing Door Bell
Under Pillow Vibrating Travel Alarm Clock
Voice Output Alarm Clock
Voice Output Watch
Liquid Level Indicator
Voice Output Thermometer
Voice Output Microwave

## Slide 79: Seating/Positioning/Mobility and Transportation Aids Available
Wheelchairs
Electric Powered Wheelchairs
Powered Scooter
Electronic Ramps
Accessible Vehicles

## Slide 80: Individual Challenge
For next week can you find out what GIDEIs are? and come up with a few examples.
GIDEIs