## Slide 1
Sensory Aids for Persons with Auditory Impairments
Damian Gordon
Cook and Hussey, Chapter 9

## Slide 2
What is Assistive Technology?
“Any product, instrument, equipment or technical system used by a disabled or elderly person, made specially or existing on the market, aimed to prevent, compensate, relieve or neutralise the deficiency, the inability or the handicap.”
International ISO-9999 Standard
Recall from a previous lecture

## Slide 3
Last Week

## Slide 4
HAAT Model
Activity
Human
Context
Activity
Output
Processor
Environmental
Interface
HTI

## Slide 5
Sensory Aids
Environment
Processor
Environmental
Interface
HTI

## Slide 6
Introduction
Following the AAC philosophy outlined previously, there are two basic approaches to auditory assistive technology
  Augmentation of an existing pathway
  Use of an alternative pathway
Notes: ere
<number>

## Slide 7
Augmentation of an Existing Pathway
When someone is hard of hearing, the primary pathway is still available, but just limited.
An amplifier is required to improve the reception of certain frequencies.
Different forms of auditory impairments result in different frequency ranges being diminished.
Notes: ere
<number>

## Slide 8
Use of Alternative Sensor Pathway
When considering alternative pathways, typically two are used
  Tactile Substitution
  Visual Substitution
Notes: ere
<number>

## Slide 9
Tactile Substitution
It is important to note that the rate of auditory input is typically much faster than the tactile alternatives.
One tactile method is the Tadoma method (typically used by people who are both deaf and blind), where the deaf person receives information by placing her hands on the speaker’s face.
Notes: ere
<number>

## Slide 10
Visual Substitution
Visual displays can take many forms.
One example is when teaching hearing impaired people to speak, they will be shown a picture of the speech signal on an oscilloscope screen, sometimes coupled with either a video or computer graphics showing the mouth forming the specific sound.
Notes: ere
<number>

## Slide 11
Manualism and Oralism
Manualism and oralism are two opposing philosophies regarding the education of the deaf.
Manualism is the education of deaf students using sign language and oralism being the education of deaf students using spoken language.
Since the beginning of the 18th century, these two philosophies have been on opposing sides of a heated debate that continues to this day, although many modern deaf educational facilities attempt to integrate both approaches.
Notes: ere
<number>

## Slide 12
Manualism and Oralism
Many members of the deaf population oppose the oralist belief that deaf people should learn English, speech, and lip-reading.
The manualists claim that the oralists neglect the psychosocial development of deaf children. In their training in articulation, which requires long tedious practice, oralism leaves students with less time and energy to advance academically and socially.
Oralists claim that manualists neglect the residual hearing in deaf children and that their emphasis on sign language isolates them from wider culture and hearing family members, thus serving to restrict them to limited subculture that leaves them unable to succeed in the general population.
Notes: ere
<number>

## Slide 13
Notes: ere
<number>

## Slide 14
Visual Substitution
Other examples of visual substitution include:
  visual alarms (e.g. a flashing light for the phone or door bell).
  Computer synthesized speech.
  Written text.
Notes: ere
<number>

## Slide 15
Examples of aids
Hearing Aids
These are relatively sophisticated devices that do not merely amplify sounds, but rather as mentioned earlier, the devices amplify frequencies that need it, and leave others alone (this will vary from individual to individual).
Average conversational speech can range from 40dB to 80dB.
Two types; air conduction and bone conduction.
Notes: ere
<number>

## Slide 16
Notes: ere
<number>

## Slide 17
Types of Hearing Aids
Notes: ere
<number>

## Slide 18
BAHA (Bone Anchored Hearing Appliance)
People with single-sided deafness can use BAHA (Bone Anchored Hearing Appliance) which contain a microphone that transmits sound from the deafened ear to the hearing ear.
Also some people are prone to chronic ear infections or ear canal malformations if they use air conduction.
Notes: ere
<number>

## Slide 19
Cochlear Implants
Designed for people with a profound hearing loss who cannot benefit from hearing aids, the cochlear implant (CI) is an electronic device that stimulates the auditory nerve with electrical signals that the brain can interpret as sound. The device is comprised of two main components: 1) the external processor, microphone and battery and 2) the surgically-implanted internal receiver with electrodes in the cochlea.
Notes: ere
<number>

## Slide 20
Basic Structure of Hearing Aids
An analogue hearing aid
Receiver
Power amp
Filter
Preamp
Analogue control
Mechanical Settings

## Slide 21
Basic Structure of Hearing Aids
A digitally controlled analogue hearing aid
Power amp
Filter
Preamp
Digital control
Programmable Memory
Programmer Interface
Receiver

## Slide 22
Basic Structure of Hearing Aids
A digital signal processing hearing aid
D/A
A/D
Digital control
Programmable Memory
Programmer Interface
Digital Signal Processing
Receiver
Notes: <number>

## Slide 23
Hearing Aids
The microphone can be directional or omnidirectional.
The amplifier’s job is to amplify the input signal (obviously), but particularly to respond to frequencies in the in human speech range.
The amplifier needs to: remove noise where possible, amplify without making the loud parts too loud, and preserve the intelligibility of the speech.

## Slide 24
Hearing Aids
Analogue Hearing Aid
  Majority of hearing aids
  The time-varying input signal is amplified and filtered if necessary
  The signal is then set directly into the speaker

## Slide 25
Hearing Aids
Digitally Controlled Analogue Hearing Aid
  The signal path is still analogue, but the control of it is by digital circuits.
  The benefit of this is that the parameters of control can be stored in digital memory, making this a very flexible type of hearing aid.
  Can be configured to meet the needs of the user.

## Slide 26
Hearing Aids
Digital Signal Processing Hearing Aid
  Same as the previous one, this stores user parameters.
  Input and output are still analogue.
  Much better at cancelling out noise.

## Slide 27
Digital Signal Processing

## Slide 28
Computing Assistance
Translators
  Speech to sign
  Sign to speech
    Gesture recognition
  Need sign language grammars
Video phones
Word processors
Speech training
  http://www.speechviewer.com/

## Slide 29
Signing Avatar Technology
“Weather is the heat we feel on a summer day. It's the rain that delays our ball game. It's the wind that blows leaves off trees. It's all these things and more. Weather is the condition of the air outside at any given time or place.”
http://www.w3.org/WAI/RD/2004/06/sims-mov.htm

## Slide 30
Signing Avatar Technology

## Slide 31
Most significant new communication device is…
The mobile phone
…with SMS

## Slide 32
Assistive Technology for Students with Hearing Impairments
Notes: <number>
This slide shows several tools that children with hearing impairments and other learning disabilities can use to help them participate more fully in educational activities. Pictured are amplification systems with hand held microphones to amplify a communication partner’s voice and other systems which specifically amplify the teacher’s voice and direct it into the student’s earpiece, headphones or hearing aid. Also pictured is a classroom amplification system can benefit all of the students in a classroom by amplifying the teachers voice and projecting it through speakers placed around the classroom.
In addition, there are adaptations that can allow students access to classroom materials and information via multimedia, telecommunication and interpretation services.
Objects pictured on this slide include:
On the left, Auditory Trainer by Phonic Ear
On the right,
Sound Wizard by HITEC
Speechmaker by Williams Sound
Portable Wireless amplification system by LightSPEED Technologies

## Slide 33
Check out the OATS site
http://www.oatsoft.org/Software/Software/by-category/Repository/Function/TextToSpeech