## Slide 1
Sensory Aids for Persons with Visual Impairments
Damian Gordon
Cook and Hussey, Chapter 8

## Slide 2
What is Assistive Technology?
“Any product, instrument, equipment or technical system used by a disabled or elderly person, made specially or existing on the market, aimed to prevent, compensate, relieve or neutralise the deficiency, the inability or the handicap.”
International ISO-9999 Standard
Recall from a previous lecture

## Slide 3
Last Week

## Slide 4
Introduction
Patients with low vision were surveyed to determine their needs for AT
149 individuals participated
The age range was 51-96 years (mean age was 76 years old)
Two thirds were male

## Slide 5
Introduction
The highest priority items were;
  Under the heading of Travel
    Finding a clear path, identifying landmarks, recognizing traffic signals, stepping off the curb
  Under the heading of Self-Care
    Applying make-up, shaving
  Under the heading of Reading
    Large print, signs, finding the correct food in the kitchen
  Under the heading of Recreation
    Television, recognizing people’s faces.

## Slide 6
HAAT Model
Activity
Human
Context
Activity
Output
Processor
Environmental
Interface
HTI

## Slide 7
Sensory Aids
Environment
Processor
Environmental
Interface
HTI

## Slide 8
Principles of Computer Adaptations
Computer interaction is bidirectional
User output is typically achieved by Visual Display
This is sometimes called Soft Copy
When output is produced from a printer, it is called Hard Copy
Computers can also provide auditory outputs in a range of ways
  sounds,
  beeps,
  music,
  synthesised speech.

## Slide 9
Types of Visual Impairment

## Slide 10
Types of Visual Impairments
Low Vision: An individual is able to use a visual display but the standard size, contrast or spacing is inadequate. (augmented technology)
Blind: An individual for whom a visual display does not provide a useful input or output. (alternative technology – may be audition [hearing] or touch)
Some specific conditions: on the following slides...

## Slide 11
Myopia and Hypermetropia
Myopia
(short-sighted)
Hypermetropia
(long-sighted)
Notes: <number>

## Slide 12
Macular degeneration

## Slide 13
Tunnel vision

## Slide 14
Diabetic retinopathy

## Slide 15
Cataracts

## Slide 16
Graphic User Interface

## Slide 17
Graphic User Interface
GUI allows non-disabled users through the keyboard or mouse for input and a visual display or speakers for output.
The GUI has three features;
  A mouse pointer which is moved across the screen
  The use of graphical menus and icons
  One of more windows

## Slide 18
Graphic User Interface
The GUI is design to save typing, reduce effort, and increases accuracy.
The use of icons generally helps with recall and ease of use.
Multiple windows can overlap.

## Slide 19
Graphic User Interface
The GUI has both advantages and disadvantages for the disabled users community.
  The benefits are the same as those that apply to non-disabled users
  The disadvantages are mainly that the user may not have the physical (eye-hand) coordination or visual skills.

## Slide 20
Graphic User Interface
Adaption for alternative input or output is is often difficult and, and adaptations may need to be redone when the underlying operating system is changed.

## Slide 21
Graphic User Interface
The GUI presents difficult problems to the blind computer user.
Early computer systems used a Command Line Interface (CLI) in which commands were typed in and then executed by the computer.
Early screen readers were able to access the memory buffer and copy the text from the screen to a speech synthesizer.

## Slide 22
Graphic User Interface
The GUI cannot be used in the same way, since it uses Visual Metaphors.
Which are familiar objects to represent actions in the computer.
For example, to delete a file you can drag it into the trash can.
A filing cabinet can be used to represent a disk drive.

## Slide 23
Graphic User Interface
The GUI represents several problems for the blind user
It is difficult to represent the visual elements in an alternative mode. How could a text-to-speech or speech synthesis program represent this complexity?

## Slide 24
Graphic User Interface
Most icons have text labels with them, and one adaptation approach is to intercept this label and send it to a text-to-speech system.

## Slide 25
Graphic User Interface
Another issue concerns the fact that the GUI is spatially organised.
Since auditory information is organised in a temporal (time-based) fashion, this poses challenges.
It is difficult to express the location of the mouse pointer by speech alone. The only exception being the extremities of the screen, e.g., top of screen, right border.

## Slide 26
Graphic User Interface
Additionally multiple, overlapping windows make sense visually, but can be complex to describe in an auditory context.

## Slide 27
Graphic User Interface
The Microsoft Application Programming Interface for accessibility is a set of programs that provide alternative ways to store and access information about the contents of the computer screen.
The accessibility API also includes software driver interfaces that provide a standard mechanism for accessibility utilities to send information to speech devices or refreshable Braille displays.

## Slide 28
Non-speech Sound Cues
Four types of non-speech sound cues that represent visual icons
  Auditory icons
  Earcons
  Hearcons
  Beacons

## Slide 29
Non-speech Sound Cues: Auditory icons
These are everyday sounds used to represent graphical objects, e.g. A window might be represented by the sound of tapping a glass pane, a text box could be represented using the sound of a typewriter.
The Screen Access Model and Windows sound libraries are used in some applications.

## Slide 30
Non-speech Sound Cues: Earcons
These are abstract auditory labels that do not necessarily have a semantic relationship to the object that they represent.
An example of an earcon is a musical note or string of notes played when a file, window, or program is open or closed.
Different musical instruments may be used to represent different actions, such as a trumpet representing opening a file, and a drum representing closing a file.

## Slide 31
Non-speech Sound Cues: Hearcons
These are either nature sounds or musical works.
Examples are running rivers or birds tweeting.
Location dependent
These typically prove to be ineffective in user tests.

## Slide 32
Non-speech Sound Cues: Beacons
These are a combination of different auditory labels to convey a series of actions.
It usually employs Gestalt presentation
  Similarity
  Proximity
  Continuation
  Etc.

## Slide 33
Reading Aids for People with Visual Impairments
Three major problems facing the visually impaired;
  Access to printed reading materials
  Orientation and mobility (moving safely and easily)
  Access to computers and the internet

## Slide 34
Reading Aids for People with Visual Impairments
Three major problems facing the visually impaired;
  Access to printed reading materials
  Orientation and mobility (moving safely and easily)
  Access to computers and the internet

## Slide 35
Interesting PhD Thesis
“Interaction with Sound: Explorations beyond the Frontiers of 3D virtual auditory Environments”
http://www.x3t.net/thesis.html

## Slide 36
Magnification Aids
Three factors that effect visual performance
  Size
  Spacing
  Contrast
Magnification can be of three types
  Vertical (increasing the size of the text)
  Horizontal (increasing the spacing of the text)
  Both

## Slide 37
Magnification Aids
Optical Aids | Non-Optical Aids | Electronic Aids
Hand-held magnifiers Stand magnifiers Field Expanders Telescopes | Enlarged print High-intensity lamps Daily Living aids High-contrast objects | CCTVs Portable CCTVs Slide Projectors Opaque projectors Microfiche readers

## Slide 38
Screen Magnifiers
Screen Magnifiers
Three basic modes of operation
  Lens magnification: A magnifier is placed over an area of the screen and that area is increased
  Part-screen magnification: Almost exactly the same as “lens magnification” except magnification happens in a separate window
  Full-screen magnification: Enlarge the entire screen

## Slide 39
Automatic Reading of books
They need the three components mentioned at the start
  An environmental interface
  An information processor
  A user display

## Slide 40
Automatic Reading of books
They need the three components mentioned at the start
  An environmental interface: OCR
  An information processor: Text-to-Speech
  A user display: Speaker

## Slide 41
Automatic Reading of books
Optical
Character
Recognition
Camera
Or
Scanner
Text-to-speech
Text-to-Braille
Voice Synthesiser
Refreshable Braille Display

## Slide 42
Recorded Audio Material
CDs and CD-ROMs
  E.g. Recording for blind and dyslexic
    http://www.rfbd.org
  E.g. National Library Service for the Blind
    http://www.loc.gov

## Slide 43
Recorded Audio Material
DAISY CONSORTIUM
  http://www.daisy.org
  This group has develop an international standard for digital talking books, which includes production, exchange, and use of digital books.
  The DAISY standard is hardware independent and operating system independent.

## Slide 44
Screenreaders
I know Ciaran is covering this in Accessible Web Design, so the quickest thing to say is look at the Wikipedia page:
“Comparison of screen readers”

## Slide 45
Screenreaders

## Slide 46
Pictures of AT Devices for Visual Impairment

## Slide 47
Large print books
Audio Books
Desk top magnifiers
Access to Print Material
Notes: <number>
Access to print can be provided through large print books, Audio books (such as books on tape) or desk top magnification. This slide shows a comparison between a regular academic textbook and an enlarged print textbook. By enlarging pictures and text, a student with a visual impairment can have greater access to the curriculum.
Discussion Prompt:
Does anyone in the audience have any questions or any experience with large print books?
How does one go about acquiring large print books? Large print and Braille books can be obtained from Michigan School for the Blind 1(800) 622-6730.

## Slide 48
Access to Writing for Students with Visual Impairments
Notes: <number>
The next slide illustrates a range of assistive technology tools for writing Braille.
Methods of writing braille can range from a slate and stylus or Perkins Brailler to the use of notetaking devices (personal digital assistants) that use either a Perkins-brailler style keyboard for data entry or a computer-style keyboard. PDA’s can have synthesized speech output, or can have both speech and refreshable braille output.
Tools featured on this slide include:
1. Perkins Brailler from Howe Press
2. Slate and Stylus from American Printing House for the Blind
3. Braille labeler
4. Type n’ Speak from Freedom Scientific
5. Braille n’ Speak from Freedom Scientific
6. Blazer Embosser from Freedom Scientific
7. Braille Notetakers: Braille note from Pulse Data, Braille Lite from Freedom Scientific, Elba form Papenmeier

## Slide 49
Lower screen resolution
High contrast settings
Screen magnification software
Screen reader software
Scan and read software
Refreshable Braille output
Computer Access for Students with Visual Impairments
Notes: <number>
For accessing a computer there are settings that can be made in the accessibility features of a Window based computer. No-cost changes can be made to the screen resolution; the lower the screen resolution, the larger items will appear on the computer monitor. There are also "high contrast" screen settings which can be made.
If the items included in Windows are not sufficient, there are screen magnification programs such as MAGIC produced by Freedom Scientific, which can afford the user more options for adjustments.
If a user is totally blind, or doesn't have enough useful vision to utilize screen enlargement, there are screen-reading programs available. These programs allow the user to operate a computer independently, and use synthesized speech, and sometimes an optional refreshable braille display to provide output of the information presented on the computer monitor. Examples of screen reading programs might include JAWS for Windows, or Window-Eyes.
Another area where a computer has been extremely useful is to give access to printed materials through use of a scanning and reading system. These programs use a standard scanner connected to your computer to scan in printed material. These packages are self-voicing and have optical character recognition (OCR) integrated into them.
These programs can be rather expensive to purchase. It's possible to put together a package of a commercial OCR program and a screen reader to get similar results, but a person needs to be familiar with computers and configuring programs to work together. Examples of these integrated packages might include Kurzweil 1000 or OpenBook. An example of a commercial package might be OmniPage Professional
Items shown on slide:
1. Windows accessibility features
2. Jaws for Windows from Freedom Scientific, Open Book Window Eyes form GW Micro, Kurzweil 1000 from Kurzweil
Educational systems, and Accessibility Suite from Premier Assistive Technology.
3. Refreshable Braille from Freedom Scientific
Discussion Prompt:
What is the difference between a screen reader and a scanning and reading system?
The difference between a screen reader and a scanning and reading system is that the screen reader is used to operate the computer independently, whereas, the scanning and reading system is used specifically to access written information.

## Slide 50
Check out the OATS site
http://www.oatsoft.org/Software/Software/by-category/Repository/Need/ViewingScreen

## Slide 51
Just for Shauna – a picture of TT